## Slide 1
TADF semiconductors
for OLEDs
How spin physics turns “wasted” triplets into useful light
Core story: voltage → excitons → spin statistics → triplet bottleneck → thermal recycling → photons
presentation + visual simulations
Notes: Open by framing TADF as a quantum engineering trick. The whole topic is about moving from electrical energy to light, and avoiding the loss of triplet excitons.

## Slide 2
The whole mechanism in one map
Use this as the mental route through the talk
1
Inject charges
electrons + holes enter organic layers
2
Make excitons
bound electron–hole excited states
3
Spin lottery
25% singlet, 75% triplet
4
Bottleneck
triplets are spin-forbidden to emit
5
TADF recycle
RISC converts T₁ back to S₁
6
Photon out
S₁ → S₀ gives fluorescence
Analogy: a factory line. Charges arrive, make excitons, most excitons enter the wrong room, and TADF builds a return route back to the light-emitting room.
Notes: Explain that the talk is not many disconnected facts. It is one factory-line story: get charges in, bind them, deal with spin, then get photons out.

## Slide 3
OLED = molecular layers that move charge and emit light
The emissive layer is where electron–hole pairs form excitons
Cathode
electron injection
Electron transport layer
moves e⁻ toward emitter
Emissive layer
exciton formation + light
Hole transport layer
moves h⁺ toward emitter
Anode / transparent contact
hole injection
Glass / substrate
lets light escape
e⁻
h⁺
Organic semiconductor ≠ silicon band picture only. It is often clearer to think in terms of molecular HOMO and LUMO levels.
Notes: Use the sandwich analogy. Different layers are not decoration; they are engineered to inject and transport electrons and holes to the emissive layer.

## Slide 4
Charges meet: electron + hole → exciton
An exciton is a bound excited state, like a loose molecular “atom”
LUMO: electron-like state
HOMO: hole-like state
energy gap → colour
of emitted photon
hν = E(S₁) − E(S₀) = hc / λ
Analogy: the electron and hole are like two opposite dancers pulled together; their paired dance is the exciton.
Notes: Define HOMO and LUMO carefully. Then say the exciton is not a real atom, but the analogy is useful: a negative electron bound to a positive hole.

## Slide 5
Spin turns one exciton into two families
Coupling electron spin and hole spin gives singlet and triplet states
electron spin ½
hole spin ½
↑
↓
S = 0
Singlet
1 state
S = 1
Triplet
3 states
S
T
T
T
spin lottery
≈25% singlet
≈75% triplet
Four doors: one leads to the singlet room, three lead to the triplet room. Random exciton formation mostly creates triplets.
Notes: Make the link to quantum mechanics: this is the same addition of two spin-one-half objects. One singlet state and three triplet projections give the famous 25/75 split.

## Slide 6
Conventional fluorescence wastes most excitons
S₁ can emit easily; T₁ is spin-forbidden to S₀
Energy
S₁
T₁
S₀
allowed
fluorescence
×
spin-forbidden
ΔS ≠ 0
Selection rule analogy: the triplet has energy to pay for a photon, but it is holding the wrong spin “passport”.
Result: ordinary fluorescent OLEDs can efficiently use the 25% singlet population, but triplets become a loss channel.
Notes: Emphasise forbidden means much less likely, not absolutely impossible. The key problem is that three-quarters of electrically generated excitons are triplets.

## Slide 7
TADF builds a return route from triplet to singlet
Thermally activated delayed fluorescence
Energy
S₁
T₁
S₀
RISC
thermal climb
photon
ISC
T₁
wait in triplet room
heat
thermal kick
S₁
back to fluorescent room
hν
photon leaves
Delayed = the photon is still fluorescence from S₁ → S₀, but it appears after the exciton detours through T₁.
Notes: Say the photon does not directly come from T1. The triplet is converted back to the singlet first. That is the recycling route.

## Slide 8
Simulation 1: why ΔEₛₜ must be small
Thermal activation drops rapidly as the S₁–T₁ gap grows
Chart: 
| 0.01 | 0.04 | 0.06 | 0.09 | 0.11 | 0.14 | 0.16 | 0.18 | 0.21 | 0.23 | 0.26 | 0.29
relative thermal activation ∝ exp(-ΔE/kT) | 0.67919 | 0.25821 | 0.098167 | 0.037321 | 0.014189 | 0.0053942 | 0.0020507 | 0.00077964 | 0.0002964 | 0.00011269 | 4.284e-05 | 1.6287e-05
At room temperature, kBT ≈ 0.026 eV. If ΔEₛₜ is only a few kBT, triplets can thermally climb back to S₁.
If ΔEₛₜ is large, the climb becomes a wall. RISC slows down and triplets are lost.
molecular target: ΔEₛₜ ≲ 0.1 eV
Notes: Use this as a qualitative simulation. The exact RISC rate is more complex, but the Boltzmann factor explains why small energy gaps matter.

## Slide 9
Molecular design: separate HOMO and LUMO just enough
Donor–acceptor molecules reduce exchange by reducing orbital overlap
Donor side: HOMO-rich
Accepts positive-hole character
Acceptor side: LUMO-rich
Hosts electron density
Twist/spacing lowers orbital overlap → smaller exchange integral → smaller ΔEₛₜ
ΔEₛₜ ∼ 2J and J ↓ when overlap ↓
Notes: Explain the balance. We want HOMO and LUMO separated enough to lower exchange, but not so separated that emission becomes weak.

## Slide 10
Simulation 2: the design trade-off
Orbital overlap helps emission but increases ΔEₛₜ
Chart: 
| 0.0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0
ΔEₛₜ tendency | 0.02 | 0.0232 | 0.0328 | 0.0488 | 0.0712 | 0.1 | 0.1352 | 0.1768 | 0.2248 | 0.2792 | 0.34
oscillator strength tendency | 0 | 0.039811 | 0.10506 | 0.18534 | 0.27726 | 0.37893 | 0.48912 | 0.60693 | 0.73169 | 0.86286 | 1
useful compromise | 0 | 0.064328 | 0.12637 | 0.17067 | 0.19106 | 0.18795 | 0.16679 | 0.13539 | 0.10136 | 0.070364 | 0.045461
Too much overlap: bright transition, but ΔEₛₜ becomes too large.
Too little overlap: tiny ΔEₛₜ, but weak light emission.
Best TADF design lives in the compromise zone.
Notes: This is a conceptual simulation, not a fitted dataset. It communicates the design tension: exchange splitting and light emission depend on orbital overlap in competing ways.

## Slide 11
Simulation 3: prompt + delayed fluorescence
Delayed emission appears after triplets recycle through RISC
Chart: 
| 0.0 | 0.2 | 0.4 | 0.6 | 0.8 | 1.0 | 1.2 | 1.4 | 1.6 | 1.8 | 2.0 | 2.2 | 2.4 | 2.6 | 2.8 | 3.0 | 3.2 | 3.4 | 3.6 | 3.8 | 4.0 | 4.2 | 4.4 | 4.6 | 4.8 | 5.0 | 5.2 | 5.4 | 5.6 | 5.8 | 6.0 | 6.2 | 6.4 | 6.6 | 6.8 | 7.0 | 7.2 | 7.4 | 7.6 | 7.8 | 8.0 | 8.2 | 8.4 | 8.6 | 8.8 | 9.0 | 9.2 | 9.4 | 9.6 | 9.8 | 10.0
prompt singlet fluorescence | 1 | 0.64118 | 0.41111 | 0.2636 | 0.16901 | 0.10837 | 0.069483 | 0.044551 | 0.028566 | 0.018316 | 0.011744 | 0.0075298 | 0.0048279 | 0.0030956 | 0.0019848 | 0.0012726 | 0.00081599 | 0.0005232 | 0.00033546 | 0.00021509 | 0.00013791 | 8.8427e-05 | 5.6698e-05 | 3.6353e-05 | 2.3309e-05 | 1.4945e-05 | 9.5827e-06 | 6.1442e-06 | 3.9395e-06 | 2.526e-06 | 1.6196e-06 | 1.0385e-06 | 6.6584e-07 | 4.2692e-07 | 2.7373e-07 | 1.7551e-07 | 1.1254e-07 | 7.2155e-08 | 4.6265e-08 | 2.9664e-08 | 1.902e-08 | 1.2195e-08 | 7.8193e-09 | 5.0136e-09 | 3.2146e-09 | 2.0612e-09 | 1.3216e-09 | 8.4737e-10 | 5.4331e-10 | 3.4836e-10 | 2.2336e-10
delayed TADF tail | 0.22 | 0.20927 | 0.19906 | 0.18936 | 0.18012 | 0.17134 | 0.16298 | 0.15503 | 0.14747 | 0.14028 | 0.13344 | 0.12693 | 0.12074 | 0.11485 | 0.10925 | 0.10392 | 0.098852 | 0.094031 | 0.089445 | 0.085083 | 0.080933 | 0.076986 | 0.073232 | 0.06966 | 0.066263 | 0.063031 | 0.059957 | 0.057033 | 0.054251 | 0.051605 | 0.049089 | 0.046695 | 0.044417 | 0.042251 | 0.04019 | 0.03823 | 0.036366 | 0.034592 | 0.032905 | 0.0313 | 0.029774 | 0.028322 | 0.02694 | 0.025627 | 0.024377 | 0.023188 | 0.022057 | 0.020981 | 0.019958 | 0.018985 | 0.018059
measured total | 1.22 | 0.85045 | 0.61018 | 0.45295 | 0.34913 | 0.2797 | 0.23246 | 0.19958 | 0.17604 | 0.15859 | 0.14518 | 0.13446 | 0.12557 | 0.11795 | 0.11123 | 0.10519 | 0.099668 | 0.094554 | 0.089781 | 0.085298 | 0.081071 | 0.077075 | 0.073288 | 0.069696 | 0.066286 | 0.063046 | 0.059967 | 0.057039 | 0.054255 | 0.051608 | 0.04909 | 0.046696 | 0.044418 | 0.042251 | 0.040191 | 0.03823 | 0.036366 | 0.034592 | 0.032905 | 0.0313 | 0.029774 | 0.028322 | 0.02694 | 0.025627 | 0.024377 | 0.023188 | 0.022057 | 0.020981 | 0.019958 | 0.018985 | 0.018059
Prompt component: excitons already in S₁ emit quickly.
Delayed component: T₁ waits, thermally returns to S₁, then emits.
Long triplet lifetimes increase collision losses, so fast RISC is desirable.
Notes: Point out that a delayed tail in transient photoluminescence is a signature of triplet recycling, but it must be interpreted carefully with other mechanisms ruled out.

## Slide 12
Device efficiency: internal ≠ external
TADF improves exciton use, but optics and losses still matter
Chart: 
| singlets only | TADF ideal | with outcoupling | real high current
relative photons out / % | 25 | 100 | 25 | 14
Internal quantum efficiency: fraction of excitons that become photons inside the device.
External quantum efficiency: photons that actually escape the OLED stack.
Roll-off: at high brightness, exciton–exciton and exciton–charge collisions reduce efficiency.
Notes: Explain that 100% internal quantum efficiency is the ideal exciton-use limit. It does not mean every electron produces a visible photon escaping the display.

## Slide 13
Good TADF molecules still need the right neighbourhood
Hosts and transport layers control where energy goes
ETL
electron transport
HOST + TADF
emitter isolated in host
HTL
hole transport
Host energy levels must confine excitons on the emitter, not steal them.
Analogy: the TADF molecule is the performer; the host is the stage, lighting, crowd control and safety barrier.
Notes: Make clear that material design is not only a molecule problem. The host and transport layers can either support or ruin the emitter.

## Slide 14
Click-through animation: charge injection
Step 1 of the mechanism
organic emissive layer
e⁻
h⁺
Electrons and holes are injected from opposite electrodes and driven toward each other.
Notes: This slide and the next few act as a built animation. Advance slide-by-slide to show the mechanism.

## Slide 15
Click-through animation: exciton formation
Step 2 of the mechanism
e⁻ + h⁺
exciton
The electron–hole pair is bound: an exciton. Now the decisive variable is spin.
Notes: Now say: forming an exciton is not the end. It can be singlet or triplet depending on spin coupling.

## Slide 16
Click-through animation: the spin lottery
Step 3 of the mechanism
S₁
25%
T₁
75% total
T₁
75% total
T₁
75% total
random formation gives one singlet door and three triplet doors
Conventional fluorescence uses the green door easily, but struggles with the three purple doors.
Notes: Use the four-door analogy. This slide explains why OLED spin statistics are such a big issue.

## Slide 17
Click-through animation: the TADF recycling route
Step 4: triplets return to singlets before emitting
T₁
triplet room
heat
S₁
light room
hν
S₀
ground
TADF does not make triplets emit directly. It converts them back into singlets, then uses ordinary fluorescence.
Notes: End the animation by stressing the most common misconception: delayed fluorescence still comes from S1 to S0. The delay comes from time spent in T1.

## Slide 18
One sentence version
Everything in the talk reduces to this chain
TADF is a quantum recycling strategy.
voltage
e⁻ + h⁺
exciton
S/T spin split
T₁ bottleneck
RISC
S₁ fluorescence
photon
Design levers: lower ΔEₛₜ, preserve oscillator strength, speed up RISC, suppress triplet losses, and engineer the host/device stack.
remember: triplets are not wasted if you can recycle them
Notes: Close by tying the physics to device design. TADF is not magic: it is the deliberate manipulation of molecular wavefunctions and excited-state kinetics.